## Slide 1
UNDERWATER ROBOTICS & AUTONOMOUS NAVIGATION
IIT Mandi
PHASE 1
PHASE 2
Dynamics Overview
MATLAB Model (exOtter / Arjun)
Presented by:
[Your Name]
[Roll No.] | [Branch]
Custom Control Deployment in ArduSub
Assignment Progress Report — Phases 1 & 2
Based on study of exOtter.m (MSS Toolbox) | 1-DOF Heave Simulation
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 2
PHASE 1 — DYNAMICS OVERVIEW
Marine Craft Motion — Two Ways Engineers Study It
1 Maneuvering
How a ship steers and turns when the captain uses the engine/steering
Studied by pretending the ship is in perfectly calm water
Focuses on horizontal movements: forward, sliding sideways, turning
Controlling the actual path the vessel takes
2 Seakeeping
How a ship gets tossed around by ocean waves
Assumes the ship is trying to maintain steady speed & straight course
Studies vertical motions: heave, pitch, roll
Understanding how waves affect the ship's stability
These two categories together cover all six degrees of freedom of a vessel.
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 3
PHASE 1 — DYNAMICS OVERVIEW
The Key Equation — M·v̇ + C(v)·v + D(v)·v + g(η) = τ
M · v̇ + C(v) · v + D(v) · v + g(η) = τ
M
Inertia Matrix
M = Mrb + Ma
Rigid body mass + Added mass
From your notes: M(Mass Matrix)
C(v)·v
Coriolis Forces
Rotational coupling
C = Crb + Ca
Twisting momentum of the heavy vessel rotating in 3D
D(v)·v
Drag / Damping
Water resistance
Non-linear at higher speeds
D(v)·v — depends on both position and velocity
g(η)
Gravity & Buoyancy
Natural desire to float
Net restoring force
Weight and distance from the water surface
τ
Thruster Force
Control input
τ = [tau-X, tau-N]
Force and torque from propellers
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 4
PHASE 1 — Q1: Added Mass
What is Added Mass and Why Does It Matter More Underwater?
Definition
When a vehicle accelerates through water, it has to drag a surrounding blob of water with it. This extra water resists being moved — making the vehicle feel heavier than it actually is. From your notes: "Added mass is the KE of the fluid that is forced to move along with the vehicle"
From your notes:
Physically, the fluid is added to the vehicle
At low speeds: oscillates, difficult to move
At high speed: becomes chaotic, multiplies aggressively
Aircraft vs Underwater Vehicle
Air density
≈ 1.2 kg/m³
Added mass negligible
Water density
≈ 1025 kg/m³
Added mass = 30–50% of vehicle mass
Why It Matters for AUVs
Makes vehicle feel much heavier than it is
Added mass must be included in M matrix: M = Mrb + Ma
Bigger mass → harder to move the boat
Smaller mass → easier to accelerate
From notes: A33 = 5.0 kg for heave direction
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 5
PHASE 1 — Q2 & Q3
Nonlinear Damping & The 6 Degrees of Freedom
Q2 Why is Damping Nonlinear at Higher Speeds?
Linear drag (low speed):
F_drag = D · v (proportional to velocity)
Nonlinear drag (high speed):
F_drag = D · v² (proportional to velocity squared)
Your notes explanation:
Damping becomes non-linear because at higher speeds, the fluid flow transitions from smooth (laminar) to turbulent
Drag grows much faster — the vehicle loses energy to the fluid rapidly
At high speed: the fluid is highly dynamic and produces chaotic drag
Linear model is only a reasonable approximation at small/slow motions
Q3 The 6 Degrees of Freedom
Surge
Forward / Backward (X)
Sway
Left / Right (Y)
Heave
Up / Down — DEPTH (Z)
KEY
Roll
Rotation about X
Pitch
Rotation about Y
Yaw
Rotation about Z — HEADING
KEY
Heave (depth) and Yaw (heading) are the two most important DOF for AUV control
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 6
PHASE 2 — MATLAB MODEL
What I Studied: exOtter.m from MSS Toolbox
exOtter.m — The Reference Model I Studied
From my notes (Phase 2, Page 1):
Ex-1 = exOtter.m → Simulates a boat (Otter USV) using MSS Toolbox
Input: Propeller forces (tau)
Output: Motion (velocity, position)
Simulation runs at 50 Hz → h = 1/50 = 0.02 sec time step
Uses EKF (Extended Kalman Filter) for state estimation
States: u, v, w (translational velocities), p, q, r (angular velocities)
phi, theta → angular positions | psi → heading
Key Variables in exOtter.m
x = [u v w p q r x y z phi theta psi]'
B_prop → Input (propeller) matrix
Binv = inv(B_prop) → Control allocation
M(6,6) → Mass matrix element
EKF_5states → Estimates [x_N, v_N, U, chi, omega]
What Binv Means (from your notes)
Binv = inv(B_prop) → action(C)
This is the mathematical model
We use this to calculate required force
Instead of requiring forces → base → required propeller speed
Binv links the problem: force needed → motor command
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 7
PHASE 2 — MATLAB MODEL
PID Controller — Pole Placement Method
tau_N = (T/K)·a_d + (1/K)·omega_d − Kp·[ ssa(chi_hat − chi_d) + Td·(omega_hat − omega_d) + (1/Ti)·z ]
P — Proportional
Kp = M(6,6) × wn²
Controls how strongly the system reacts to error (chi_hat - chi_d)
Bigger Kp → reacts faster but may overshoot
Your notes: Kp controls how hard to push
Big error → big correction immediately
D — Derivative
Kd = M(6,6) × (2×zeta×wn − 1/T) Td = Kd / Kp
Adds damping — slows down if approaching too fast
Looks at rate of change of error (omega_hat − omega_d)
Your notes: Kd adds slowing
Prevents overshoot and oscillation
I — Integral
Ti = 10 / wn z = z + h × ssa(chi_hat − chi_d)
Fixes small long-term errors that keep happening
From your notes: 'Integral fixes steady-state error'
Small errors accumulate → z builds up → fixes it
z = 0 at start, then it stores accumulated errors
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 8
PHASE 2 — MATLAB MODEL
Reference Model, Tuning & Propeller Dynamics
Reference Model — Why We Need It
Without a reference model → Sudden jump → difficult to control Reference model is like a filter — smooth input → smooth desired motion
Parameters (from your notes):
wn_d = 1.0
Natural frequency of reference system
zeta_d = 1.0
Damping — Controls oscillation smoothness
r_max = deg2rad(10)
Maximum turning rate limit
chi_d = 0
Desired course direction (starts at 0)
omega_d = 0
Desired course rate (starts at 0)
a_d = 0
Desired course acceleration (starts at 0)
Zeta (damping):
zeta < 1 → oscillates | zeta = 1 → perfectly smooth | zeta > 1 → very close, no oscillation
Propeller Dynamics (from your notes)
Tn = 0.1 s
Propeller time constant — how fast propeller responds
n = [0 0]'
Initial propeller speeds: left=0, right=0
n_c = sign(u)×sqrt(|u|)
Desired propeller speed from control
n updated by Euler:
n = n − h/Tn × (n − n_c)
Load Condition & Ocean Current
mp = 25 kg
Payload mass (max 45 kg) — extra weight on boat
rp = [0.05 0 -0.35]'
Location of payload on the boat
V_c = 0
Current speed — set to 0 (no current)
beta_c = 30° (π/180)
Current direction — 30 degrees
Understanding:
This action defines extra weight on the boat and the environment that can affect its motion
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 9
PHASE 2 — MATLAB MODEL
State Estimation: EKF + simdata Table
EKF — Extended Kalman Filter (State Estimation)
From your notes:
EKF estimates the state — it does NOT control the boat
Uses GPS sensor data to estimate where the boat is
x_hat = [x_N, v_N, U, chi, omega]' → 5 states
1→ estimated x position (North)
2→ estimated y position (v_N)
3→ estimated speed (U)
4→ estimated course angle (chi)
5→ estimated turning rate (omega)
Covariance matrices from your notes:
Qd = 500 × diag([1000 1000]) | Rd = 0.00000001 × diag([1,1])
simdata Table — How Data is Stored
simdata = zeros(length(t), 19)
From your notes: 'Big purposeful data saves all important values into a table' Row 1 = first time step data | Row 2 = time step 2 data
Cols 1–12:
x = [u,v,w,p,q,r,x,y,z,phi,theta,psi]
Cols 13–17:
x_hat from EKF (5 states)
Cols 18–19:
n = [n1, n2] propeller speeds
RK4 — Runge-Kutta 4th Order Integration
x = rk4(@otter, h, x, n, mp, rp, V_c, beta_c)
RK4 is a numerical method to solve differential equations
Better accuracy than Euler (4 slope estimates per step)
From your notes: 'It is almost mini-calculations using the estimate motion using 4 directions'
Used for main vehicle dynamics — Euler used for simpler updates (z, n)
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 10
PHASE 2 — MY OWN MODEL
heave_1DOF.m — My 1-DOF Heave Simulation
(m + A₃₃) · ẇ + D₃₃ · w = τ_heave
My Model Parameters
m = 11.5 kg
Vehicle mass
A33 = 5.0 kg
Added mass in heave direction
D33 = 25.0 kg/s
Linear damping coefficient
M_heave = m + A33 = 16.5 kg
Total effective inertia
h = 0.01 s
Time step (Euler integration)
T_final = 20 s
Simulation duration
t_step = 2 s
Force switches ON at 2 seconds
F_step = 10 N
Step thruster force applied
The Euler Loop — Heart of the Simulation
Step 1 — Acceleration:
w_dot = (tau_heave − D33×w) / M_heave Newton's 2nd law: a = F_net / mass
Step 2 — Rate of depth:
z_dot = w(i) Depth changes at same rate as velocity
Step 3 — Euler update:
w(i+1) = w(i) + h × w_dot z(i+1) = z(i) + h × z_dot
Step 4 — Analytical check:
w_ss = tau / D33 = 10/25 = 0.4 m/s Terminal velocity — confirms simulation correct
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 11
PHASE 2 — RESULTS
Simulation Output — 3 Plots from heave_1DOF.m
Plot 1 Depth vs Time
[INSERT MATLAB PLOT 1 HERE — depth (m) vs time (s)]
Screenshot from MATLAB here
Depth = 0 m for first 2 s
After t=2s: depth increases continuously
No controller → depth grows without bound
This motivates Phase 3: PID control
Plot 2 Heave Velocity vs Time
[INSERT MATLAB PLOT 2 HERE — velocity (m/s) vs time (s)]
Screenshot from MATLAB here
Starts at 0 m/s at rest
Rises rapidly after force applied at t=2s
Levels off at terminal: w = 0.4 m/s
w_ss = tau/D33 = 10/25 = 0.4 m/s
Plot 3 Thruster Force vs Time
[INSERT MATLAB PLOT 3 HERE — force (N) vs time (s)]
Screenshot from MATLAB here
Zero force for t < 2 s
Step jump to 10 N at t = 2 s
Constant — this is open-loop
Confirms step input applied correctly
IIT Mandi | Underwater Robotics and Autonomous Navigation

## Slide 12
Summary & What I Learned
Phases 1 & 2 — Based on my own study notes
PHASE 1 — Dynamics Overview
✓ Studied two ways engineers analyze ships: Maneuvering vs Seakeeping
✓ Understood the full 6-DOF equation: M·v̇ + C(v)·v + D(v)·v + g(η) = τ
✓ Added Mass: vehicle drags water → feels heavier (A33 = 30-50% of mass)
✓ Nonlinear damping: turbulent flow at high speed → drag grows as v²
✓ 6 DOF identified: Heave (depth) and Yaw (heading) are most critical
✓ Understood M matrix, Coriolis, Drag, Gravity/Buoyancy, and τ
PHASE 2 — MATLAB Model
✓ Studied exOtter.m from MSS Toolbox in detail (EKF, PID, reference model)
✓ Understood EKF: estimates [x_N, v_N, U, chi, omega] from GPS data
✓ Understood PID pole placement: Kp, Kd, Ti, reference model wn_d=1, zeta_d=1
✓ Built my own heave_1DOF.m — 1-DOF depth simulation from scratch
✓ Applied 10N step force: vehicle sinks, velocity → terminal 0.4 m/s
✓ Verified: w_ss = tau/D33 = 10/25 = 0.4 m/s (analytical = simulated)
Coming Next:
Phase 3: PID Depth Controller
Phase 4: ArduSub Codebase Map
Phase 5: Custom UserCode.cpp
Phase 6: SITL Build & Test
Thank You